## Slide 1: HOW TO PROTECT YOUR HANDS IN NUCLEAR MEDICINE WORK
ICRP Publication 106 Annex E
The membership of the Working Party that prepared Annex E of ICRP Publication 106 was:
J. Liniecki (Chair) J. Jankowski C. Martin S. Mattsson
Author for educational slides on behalf of ICRP
S. Carlsson, M. Andersson

## Slide 2: Sources of exposure
Exposure from external sources (vials, syringes)
Contamination (dispensing, administration)
Slides 2-5 refer to chapter E.1

## Slide 3: Radionuclides in diagnosis: planar and SPECT
Nuclide | T1/2 | Decay mode (% abundance) | Photo emission (keV) (% abundance)
67Ga | 3.7 d | EC (100) | 93 (39 %); 185 (21 %); 300 (17 %)
75Se | 119.7 d | EC (100) | 265 (59 %); 136 (58 %); 280 (25 %)
99mTc | 6.0 h | IT (100) | 141 (89 %)
111In | 2.8 d | EC (100) | 245 (94 %); 171 (91 %)
123I | 13.3 h | EC (100) | 159 (83 %); 529 (1.4 %)
131I | 8.0 d | B- (100) | 364 (82 %); 637 (7 %)
201Tl | 72.9 h | EC (100) | 167 (10 %); 69-80 (several X-rays)
Nuclide data from ICRP Publication 107

## Slide 4: Radionuclides in diagnosis: PET
Nuclide | T1/2 (min) | Decay (% β+ ) | β+ Energy (MeV) Max. Mean |  | Range in water (mm) Max. Mean | 
18F | 109.77 | 96.7 | 0.6335 | 0.2498 | 2.4 | 0.6
64Cu | 762 | 17.41 | 0.6531 | 0.2782 | 2.9 | 0.64
11C | 20.39 | 99.77 | 0.9602 | 0.3856 | 4.1 | 1.1
13N | 9.97 | 99.8 | 1.1985 | 0.4918 | 5.1 | 1.5
15O | 2.037 | 99.9 | 1.732 | 0.7354 | 7.3 | 2.5
75Br | 96.7 | 73.0 | 2.01 | 0.719 | 8.4 | 2.6
68Ga | 67.7 | 88.9 | 1.8991 | 0.8329 | 8,2 | 2.9
124I | 6013 | 11.7 10.8 | 1.5323 2.1376 | 0.6871 0.9748 | 6.3 8.7 | 2.3 3.5
62Cu | 9.67 | 97.81 | 2.926 | 1.313 | 11.9 | 5.0
82Rb | 1.27 | 81.8 13.1 | 3.379 2.5795 | 1.534 1.167 | 14.1 10.5 | 5.9 4.3
86Y | 884 | 11.9 5.6 | 1.2535 3.141 | 0.535 0.681 | 5.2 12,7 | 1.8 2.9
66Ga | 569 | 55.3 | 4.153 | 1.739 | 16.7 | 7.4
Nuclide data from ICRP Publication 107

## Slide 5: RADIONUCLIDES IN THERAPY
Nuclide | T1/2 | Emax (MeV) and type of decay | Accompanying gamma-emission (keV)
β- -emitters |  |  | 
32P | 14.3 d | 1.7 (β-) | -
89Sr | 50.5 d | 1.5 (β-) | -
90Y | 2.7 d | 2.3 (β-) | -
131I | 8.0 d | 0.8 (β-) | 364 (82 %); 637(7 %)
153Sm | 1.9 d | 0.8 (β-) | 103 (30 %)
177Lu | 6.6 d | 0.5 (β-) | 208 (11 %); 113 (6 %)
186Re | 3.7 d | 1.1 (β-) | 137 (9 %)
188Re | 0.7 d | 2.1 (β-) | 155 (16 %)
α-emitters |  |  | 
211At | 7.2 h | 5.9 (α) | -
212Bi | 1.0 h | 6.1 (α) | 727 (7 %)
223Ra | 11.4 d | 5.87 (α) | 269 (14 %);154 (6 %)
225Ac | 10.0 d | 5.8 (α) | 
Auger electron emitters |  |  | 
67Ga | 3.3 d | Auger electrons | 93 (39 %); 185 (21 %); 300 (17 %)
125I | 59.4 d | Auger electrons | 35 (6.7 %)
195mPt | 4.0 d | Auger electrons | 99 (11 %)
Nuclide data from ICRP Publication 107

## Slide 6: APPLY ICRP BASIC SYSTEM OF RADIATION PROTECTION
(JUSTIFICATION)
OPTIMISATION APPLIED TO WORKING PROCEDURES
DOSE LIMITATION
Slide refer to chapter E.9

## Slide 7: DOSE LIMITATION
Annual equivalent dose
Skin 500 mSv averaged over 1cm2
Hands and feet 500 mSv
Slides 7-13 refer to chapter E.4
Image: ICRP Publication 103

## Slide 8: Dose limits can easily be exceeded
The equivalent dose-rate to the unprotected fingers holding a vial containing 2 GBq 18F is in the order of 200 μSv/s. If we assume that the content is dispensed to 3 patients and the time required is 10s per procedure, then the total dose to the fingers of the worker will be 4 mSv. If the procedure is repeated 5 days per week and 45 weeks per year the annual equivalent dose will be 900 mSv.
Assume an activity of 40 GBq 99mTc in a volume of 10 ml. One microdrop (20µl) of the solution will then contain an activity of 80 MBq. If spread over 10 mm2 on the skin the initial dose rate will be about 2000 mSv/h. If not removed the cumulative dose will be 17 Sv over the 10 mm2 area, i.e. 1700 mSv averaged over 1 cm2, which exceeds the dose limit of 500 mGy.

## Slide 9
Contact of an unshielded (5 ml) syringe
Dose rate at contact
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 10: Time
Dose is proportional to
the time exposed
Dose = Dose-rate x Time
Experienced workers will generally but not necessarily have lower exposure of the hands. TRAINING IS ESSENTIAL!!

## Slide 11
Time (min) to reach 500 mSv
Contact of an unshielded (5 ml) syringe
Dose rate at contact
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 12: Protection measures to reduce (optimise) external exposure of hands
Shielding
Time (training)
Distance

## Slide 13: Distance
Chart: Relative dose-rate
| 1 | 2 | 3 | 4 | 5
Y-värden | 100 | 25 | 11.1111 | 6.25 | 4
Inverse square law (ISL):
Dose-rate 1/(distance)2
Relative distance
Meaning that if the distance doubles will the dose rate is reduced to one quarter.

## Slide 14: Syringe shield
400 MBq Tc-99m in 1 ml
Not shielded
0.4 mSv/h
0.8 mSv/h
4.2 mSv/h
22 mSv/h
8 mSv/h
Shielded (2 mm W)
0.004 mSv/h
0.01 mSv/h
0.04 mSv/h
0.16 mSv/h
6 mSv/h
Slides 14-23 refer to chapter E.5

## Slide 15: Vial shield
560 mGy/h
1 mGy/h
99mTc
10 GBq
10 ml
2 mm lead

## Slide 16: RECOMMENDATION
Never touch an unshielded source with your hands
Use long tweezers for handling of sources

## Slide 17: SHIELDING OF SOURCES
Factors affecting the design:
Radionuclide (type and energy of emitted radiation)
activity
shielding material

## Slide 18: Shielding
Bench top shield
Vial shields
Syringe shields
Note:The full garment in the photo is for aseptic or good manufacturing purposes and not necessarily for radiation protection

## Slide 19: DEFINITIONS
Dose rate constant
The dose rate , Γ(μSv/h), at 1 m from a point source of 1 MBq
TVL
Tenth value layer, which is the thickness of a material that reduces the number of incident photons by a factor of 10.

## Slide 20: SPECIFIC DOSE-RATE CONSTANT (Γ) FOR SOME RADIONUCLIDES AND THE TENTH VALUE LAYER OF LEAD. DATA FROM LM UNGER & DK TRUBEY, SPECIFIC GAMMA-RAY DOSE CONSTANTS FOR NUCLIDES IMPORTANT TO DOSIMETRY AND RADIOLOGICAL ASSESSMENT, OAK RIDGE NATIONAL LABORATORY, ORNL/RSIC-45/R1 (1982)
Radionuclide | Γ (μSvh-1MBq-1) | TVL (mm lead)
F-18 | 0,1851 | 13.5
Cr-51 | 0,0063 | 6.0
Co-57 | 0.0409 | 0.57
Ga-67 | 0,0300 | 4.8
Se-75 | 0,2323 | 2.5
Mo-99 | 0,0305 | 19.7
Tc-99m | 0,0332 | 0.83
In-111 | 0,1356 | 2.23
I-123 | 0,0748 | 1.19
I-125 | 0,0743 | 0.06
I-131 | 0,0764 | 9.5
Sm-153 | 0,0244 | 0.32
Tl-201 | 0,0236 | 0.88
SHIELDING CALCULATIONS

## Slide 21: EXAMPLE 1
Estimate the thickness of a lead container for 30 GBq
of 99MTc. Dose rate at 1 m should be 2 μSv/h
Dose rate constant: 0.017 μSv/(h*MBq)
TVL: 0.9 mm lead
Dose rate for unshielded source: 0.017 μSv/(h*MBq) * 30000 MBq = 510 μSv/h
Reduce exposure 255 times which equals: ln(255)/ln(10) = 2.4 TVL = 2.2 mm lead.

## Slide 22: EXAMPLE 2
What thickness of lead is required to reduce the exposure rate to 20 μSv/h at 1 m for a container designed to store 15 GBq 131I?
According to table Γ=0.0764 μSvh-1MBq-1 for 131I which means that the unshielded dose rate at 1 m will be 15000x0.0764=1146 μSvh-1 . The shield should then be designed to reduce the dose-rate a factor of 1146/20=57.3. which will be achieved by ln(57.3)/ln(10)=1.76 * TVL From table we learn that TVL for I-131 is 9.5 mm. Hence, a shield thickness of 1.76*9.5=16.7 mm of lead is required.

## Slide 23: EXAMPLE 3
A vial containing 2 GBq 18F is put in a 2 mm lead shield generally used for 99mTc sources. How much will this shield reduce the dose-rate at the surface?
According to table TVL for 18F is 13.5 mm lead. Then the attenuation coefficient will be ln(10)/TVL=0.1706 mm-1. Assuming monoexponential attenuation, the dose-rate (D) will be reduced to: D/D0=exp(-0.1706*2)=0.71 of the unshielded dose-rate (D0).
This example shows the importance of selecting shields aimed for the source to use.

## Slide 24: SHIELDING IN PET
Biodex Medical
Protection against high energy photons requires lead and lead glass shield of significant thickness (cm)
Slide refer to chapter E.8

## Slide 25: SHIELDING AGAINST HIGH ENERGY β-PARTICLES
90Y
Max energy 2.3 MeV
Polymetylmetakrylat (PMMA) density 1188 mg/cm3 Maximum range ≈1 cm
In conclusion:
Use 1 cm of PMMA with an external layer of a few mm of lead in vial and syringe shields.
Slides 25-27 refer to chapter E.7
Take home message:
The low z material stops beta and the high z material stops the created photons from the beta.
Bremsstrahlung is generated in the source and PMMA.

## Slide 26: THE EFFECT OF SHIELDING
Procedures | Shield | Shielding efficiency
99mTc preparation | Yes No | 4.3
99mTc administration | Yes No | 1.8
18F preparation | Yes No | 2.3
18F administration | Yes No | 5.0
90Y-Zevalin® preparation | Yes No | -
90Y-Zevalin® administration | Yes No | 3.1
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 27
Summary shielding recommendations
For the injection (syringe shielding):
2 mm W (or Pb) for 99mTc give a dose reduction of at least 2 order of magnitudes.
5 mm W provides up to a factor 10 in dose reduction for 18F (8 mm W up to a factor 40).
For 90Y 10 mm PMMA completely shield beta radiation, nevertheless 5 mm shielding of tungsten provides a better shielding cutting down bremsstrahlung radiation too.
For the preparation (vial shielding):
For 18F, 3 cm of Pb provides 2 order of magnitudes on dose reduction. The same attenuation for 99mTc is obtained with 2 mm Pb.
For 90Y an acceptable shielding is obtained with 10 mm PMMA with an external layer of few mm of lead or alternatively 5 mm of W.
For 131I, 2 cm of Pb provides 2 order of magnitudes on dose reduction
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 28
Examples of good working procedures
Preparation of 99mTc
Preparation of 18F
Administration of 18F
Administration of 99mTc
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)
Slides 28-29 refer to chapter E.3

## Slide 29
Preparation of 99mTc
Examples of bad working procedures
Preparation of 18F
Administration of 18F
Administration of 99mTc
Unshielded vial and syringe
Unshielded syringe, thumb directly exposed
Unshielded syringe
Left hand holding the part of the needle
Unshielded syringe
Unshielded syringe
Unprotected fingertips
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 30: MONITORING EXTERNAL EXPOSURE
The operational quantity for external individual monitoring is the personal dose equivalent, Hp(d), which is the dose equivalent in ICRU soft tissue at an appropriate depth, d, below a specified point on the human body.
For skin, hands, and feet personal dose equivalent, Hp(0.07), a depth d=0.07 mm is used.
Slides 30-32 refer to chapter E.10

## Slide 31: MONITORING EQUIPMENT
Wrist TLD Ring TLD
Electronic extremity Electronic extremity dosimeter dosimeter
+ comfortable
delayed reading
+direct reading - uncomfortable

## Slide 32: What to measure?
The maximum dose should be evaluated and tested for conformity with the dose limit
Hand dose distribution for worker T3E, for preparation of 18F. Each curve corresponds to individual sets of 22 TL readings.
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 33: WHERE TO MEASURE?
The most exposed part of the hands are likely to be the tips of the index and middle fingers and the thumb of the dominant hand.
Based on monitoring results it is recommended that a ring dosimeter should be worn on the middle finger of the dominant hand with the element on the palm side, and that a factor of three should be applied to derive an estimate of the dose to the tip (maximum dose and fraction of dose limit). When gloves are worn the ring dosimeter should be worn under the gloves. If the dosimeter element is worn facing the back side of the hand, a factor of six should be applied.
Slides 33-35 refer to chapter E.10

## Slide 34: External exposure of hands
(Carnicer, A. et al. Occupational Exposure: With Special Reference to Skin Doses in Hands and Fingers. In Radiation Protection in Nuclear Medicine (Ed) Mattsson, S. Hoeschen,C. Springer 2013)

## Slide 35: External exposure of hands
Gauri S. Pant et. al., JNMT 2006
Figure shows that the dose is substantially higher to finger tips than the base of the fingers

## Slide 36: CONTAMINATION
Clean handprint Contaminated handprint

## Slide 37: Contamination of the worker related to:
spills
drawing dose
administration of radiopharmaceutical
experimental work with animals
emergency surgery of a therapy patient
autopsy of a therapy patient
other accidents

## Slide 38: CONTAMINATION FROM PATIENT
Excretion Concentration Contamination
Saliva <2 MBq/g utensils 2 kBq
Perspiration <20 Bq/cm2 surfaces 10 Bq/cm2
Breathing 100 Bq/l air 1 Bq/l
Urine <500 kBq/ml toilet 2 kBq/cm2
Administered activity: 1000 MBq I-131
Generally larger than the derived limits for contamination
given by ICRP (publ. 57)

## Slide 39: Skin exposure by contamination
Radionuclide | mSv-cm2/MBq-h | Radionuclide | mSv-cm2/MBq-h
14C | 305 | 90Sr-90Y (equilibrium) | 4272
18 F | 1900 | 99mTc | 243
22Na | 1870 | 111In | 376
24Na | 2357 | 123I | 365
32P | 2397 | 125I | 417
35S | 332 | 131I | 1694
36Cl | 2178 | 137Cs-137Ba (equilibrium) | 1941
45Ca | 884 | 147Pm | 612
57Co | 78 | 153Sm | 1600
59Fe | 1283 | 192Ir | 1592
60Co | 1146 | 201 Tl | 343
67Ga | 324 | 204Tl | 1804
Skin contamination equivalent dose rate factors at a depth of 70 µm
DELACROIX, D., GUERRE, J.P., LEBLANC, P., HICKMAN, C., Radionuclide and Radiation Protection Data Handbook 1998, Radiation Protection Dosimetry, Vol. 76 Nos. 1-2 1998.

## Slide 40: Decontamination of skin
If contamination of the skin occurs, immediately the area should be thoroughly washed using mild soap and tepid (not hot) water. Particular care should be paid to cleaning under the fingernails. If this does not bring the contamination to an acceptably low level the procedure should be repeated. Scrub with a nail brush but take care not to break the skin.

## Slide 41: DECONTAMINATION OF SKIN
Remaining activity (%)
Method
Substance 1 2 3 4
---------------------------------------------------------------------------------
99mTc-DTPA 1 0 1 1
99mTc-MDP 7 1 3 5
99mTc-pertechnetate 5 7 5 7
99mTc-colloid <1 <1 <1 <1
131I-Hippuran <1 <1 <1 <1
131I-iodide 8 5 <1 2
67Ga-citrate 3 1 4 1
111In-DTPA <1 <1 <1 <1
---------------------------------------------------------------------------------
1: 90 s in water, 2: 90 s in soap and water, 3: skin lotion
and 90 s in soap and water, 4: commercial decontamination
substance
IAEA, 2000. Training Material on Radiation Protection in Nuclear Medicine, Part 5. Occupational Exposure Protection of the Worker

## Slide 42: Skin exposure by contamination
In 10 months 560 inspections were carried out. Local contamination was found on the fingers of nuclear medicine technologists in 40 cases. The measured activities ranged from 211 Bq/cm2 to 460 kBq/cm2, resulting in cumulated skin doses between 0.02 and 809 mSv.
(Covens P, et al Nucl Med Com 33, 2012)

## Slide 43: - adopt clean operating conditions - adopt good laboratory practices - do not eat, smoke etc… - use nitrile or vinyl gloves (no latex) and protective clothing
To minimize contamination

## Slide 44: PROTECTIVE CLOTHING
Appropriate clothing should as a minimum include lab coat and gloves. National regulations may require more.
Notes: The image to the right is an example of clothing if the preparation of radiopharmaceuticals have to be done in a sterile environment

## Slide 45: SAFETY EQUIPMENT (OPTIMISATION) PREPARING AND DISPENSING RADIOPHARMACEUTICALS
Shields
Protective clothing
Tools for remote handling
of radioactive material
Shielded containers for radioactive waste
Dose rate monitor with alarm
Contamination monitor
Decontamination kit
Signs, labels and records

## Slide 46: SAFETY EQUIPMENT (OPTIMISATION) ADMINISTRATION OF RADIOPHARMACEUTICALS
Syringe shield
Gloves
Lead apron
Absorbing pads

## Slide 47: Recommendations (ICRP 106)
The dispensing protocol and the use of shielding devices in any radiopharmacy should be assessed carefully to optimise the strategy.
Shielding of the syringe is the most important factor affecting finger dose, and syringe shields should be used as much as possible.
Vials from which radioactive liquid is withdrawn should always be shielded.
The choice of manipulation technique only has a minor influence on finger dose; the most important factor is that staff are able to use the technique effectively.
All staff should undergo a period of intense training in which they practice manipulations using non-radioactive liquid prior to undertaking any dispensing of radioactive liquid.
Careful positioning of materials within the dispensing cabinet is important for streamlining the procedure and minimising doses to the hands.
Slides 47-49 refer to chapter E.11

## Slide 48: Recommendations (ICRP 106)
The most exposed parts of the hands are likely to be the tips of the index and middle fingers, and the thumb of the dominant hand, with exposure for the index finger being highest.
Preliminary finger dose monitoring should be undertaken for any person handling >2 GBq/day, and regular monitoring should be carried out if doses to the most exposed part of the hand exceed 6 mSv/month.
The finger tip or most exposed part of the hand should be monitored wherever possible, particularly if the dose is likely to approach a dose limit.
If it is not possible to monitor the dose to the most exposed finger tip, an empirical multiplying factor may be applied to doses recorded by ring dosimeters worn on the middle finger of the dominant hand to estimate this dose. Factors of three or six should be used for the dosimeter element on the palm or back of the hand, respectively.
The dispensing technique should be reviewed to confirm that the positions where dosimeters are worn are the most appropriate.
For injections, prior venous cannulation allows the injection to proceed more rapidly; if the syringe is shielded, the dose to the hand of the nurse or physician will be kept to a minimum.

## Slide 49: Recommendations (ICRP 106)
Significant doses can be received from a single administration of a therapy involving a high-energy beta-particle emitter, and the following precautions are recommended:
Administrations of beta-emitting therapy radiopharmaceuticals should be carefully planned.
5–10 mm thick PMMA syringe shields should always be used for administration of 90Y or similar high-energy beta-emitting therapy radionuclides.
Close contact with any thin-walled vessel containing therapeutic levels of 90Y should be avoided through the use of forceps or PMMA shielding.
Doses to the most exposed finger tips should be monitored directly for each session in which 90Y or similar high-energy beta-emitting therapy radionuclides are administered.

## Slide 50: Thank you
You are invited to use this lesson for training and to apply them in practice but not for commercial purposes.

## Slide 51
www.icrp.org